| Agency | Engine | Engine Type | Status | Dates 19__ | Arrangement | Weight (lbs) | Thrust (lbs) | RPM | SPC (lbs/hr-lbs) | Length (in) | Diameter (in) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Yokosuka | No name | TJ | E | 42-43 | r-Oc-a |  |  |  |  |  |  |
| Yokosuka | TR-10 | TJ | E | 43-44 | r-Oc-a |  | 770 |  |  |  |  |
| Yokosuka | TR-12 | TJ |  | 43-44 | 4a-r-Oc-a |  |  |  |  |  |  |
| Yokosuka | TR-12B | TJ | E | 44-45 | 4a-r-Oc-a | 700 |  |  |  |  |  |
| Yokosuka | TR-30 | TJ | E | 43-44 | 4a-r-Oc-a |  |  |  |  |  |  |
| Yokosuka | Ne-20 | TJ | S | 44-45 | 8a-Oc-a | 1000 | 1100 | 11000 | 1.36 | 106.5 | 24.4 |
| Ishikawa | Ne-140 | TJ | P | 44 | a-?-? |  |  |  |  |  |  |
| Ishikawa | Ne-130 | TJ | E | 44-45 | a-?-? | 1980 | 1980 | 9000 | 1.28 | 151.5 | 33.4 |
| Ishikawa | GTPR | TJ | P | 39-44 | p-12a-Oc-5a | 5000 | 5000 bhp @373mph | 5000 |  | 216 | 31.5 |
| Hitachi | Ne-230 | TJ | E | 44-45 | Axial compressor | 1920 | 1950 | 8100 | 1.33 | 135 | 35.9x30 |
| Mitsubishi | Ne-330 | TJ | E | 44-45 | Axial compressor | 2640 | 2860 | 7600 | 1.40 | 158 | 46.5x34.6 |
| Yokosuka | TSU-11 | CAM2 | S | 42-45 | Engine-compressor | 440 | 440 | 3000 eng/9000 comp | 4.3 | 86.7 | 25.2 |
| Hitachi | MTPR | TJ | P | 42-44 | turbojet |  |  |  |  |  |  |
| Yokosuka | KR-101 | Rocket | S | 44-45 | Liquid rocket | 375 | 3300 | Pump 14500 | 2.1 | 98.5 | 35.4x25.6 |
| Yokosuka | KA-10 | Pulse | E | 44-45 | Argus type | 330 | 990 | -- | 2.6 | 146 | 22.8 |

1—The KR-10 was a clone design based on the Walther HWK 109-509 bi-propellant rocket engine which powered the Me-163B “Komet” fighter.

2—The “Campini” type jet engine is odd enough(in 2008) to require a brief explanation.  The basic design consisted of a piston engine driving a compressor.  Fuel was injected into the air stream coming from the compressor to provide more heat and jet thrust.  Sometimes the piston engine also drove a propeller, but sometimes not.  There was no exhaust turbine nor any potential for turbine blade failures, a problem which plagued early turbojet designs.

The most famous airplane powered by this type of engine was the two-seat experimental Italian aircraft, the Caproni-Campini N-1, which first flew in 1940.  A hand-built biplane with a similar engine design had flown(after a fashion, it then crashed) in 1910, product of a Romanian designer, pilot and engineer living in Paris, Henri Coanda.  Engines of this type are today often referred to as a “motorjet” or “thermojet” engine.  The fundamental problem of the type, as I understand it(I’m not an aeronautical or aerodynamic engineer) is that the competing turbojets were not encumbered by a whole piston engine, but instead relied on a light and compact arrangement of turbine and compressor disks.  If you could get them to run reliably at the temperatures involved, turbojets were a fundamentally better bet, as the Japanese discovered for themselves.  The Soviets also built some planes with this type of powerplant, an example being the prototype Mikoyan I-250/N.

Yokosuka=First Naval Air Technical Arsenal at Yokosuka; they handled a wide range of technical, test flight and design tasks for the Imperial Navy.  Among other things, they designed the D4Y1-4 “Judy” dive bombers which were manufactured by Aichi Ltd in Southern Japan as well as the land-based P1Y1 “Frances” twin-engined bomber.

Ishikawa=Ishikawajima-Harima

Status, e=experimental, s=series(built in modest numbers), p=projected(but not built)

Arrangement: reading from left to right(the purported direction of the airflow), p=propeller, r=radial(centrifugal) compressor, a=axial compressor or turbine(some with number of stages), Oc=annular combustion chamber

Pulse=Pulsejet or Lorin Duct, similar in layout to the Argus 014 which powered the V-1 “Buzz-Bomb” cruise missile.  It was cheap to manufacture and simple, but it had major problems with flexibility, noise and vibration.  When Messerschmidt tried to air launch an Me-328 prototype with two pulsejets, once they were started the harrowing vibration from two such engines tore the little plane apart.  After building some V-1(or FZG-76) prototypes with a seat for a pilot and manual controls as part of the V-1 development program, the German Air Force went on to build manned versions of the V-1 as the “Reichenberg” manned bomb.  If they had been used operationally, they would have worked a lot like the Ohka(or the American flying bombs of “Project Aphrodite”), but Hitler quashed the project.